## Slide 1: Sensing and Perception Vision Sensors
Manfred Huber
Fall 2019

## Slide 2: Proximity Sensors
Proximity / Distance sensors such as Sonar, Laser Ranger, LADAR, etc. are good at:
  Determining the presence of an obstacle / object
  Measuring the distance to this obstacle
  Forming a map of the surrounding environment in terms of occupied space at a fixed level
They have problems with:
  Identifying the object
  Differentiating multiple objects
  Mapping in full 3D (need to tilt the sensor)

## Slide 3: Machine Vision
Machine vision uses a passive sensor to detect and identify an object
  Cameras detect objects with no need to transmit a signal
    Hard to detect by a third party
    Multiple cameras can be used without interference
Machine vision requires significant amounts of computer processing to extract information

## Slide 4: Machine Vision
By identifying and classifying groups of pixels as an obstacle, machine vision can be used to generate information that supports path planning or opportunistic motion behaviors.
Vision with a single camera usually requires assumptions about the terrain to work

## Slide 5: Machine Vision
Many ways to process images or video have been developed
A common processing sequence to identify an object (object recognition) involves
Filtering
Feature
Detection
Segmentation
“Box”
Recognition
Early Vision

## Slide 6: Machine Vision
Filtering:
  Remove noise, normalize, and emphasize the image
Feature Detection:
  Extract significant local structures
    Edges, Color, Texture, Motion, …
Segmentation:
  Group features into regions belonging to a common object
Recognition:
  Determine identity of the object

## Slide 7: Machine Vision
Common example for simple color-based object extraction:
  Filtering:
    Blur image to reduce noise in individual pixels
  Feature Detection:
    Identify pixels that are within a given color range
      Results in a black and white feature map
  Segmentation:
    Blob coloring to link neighboring pixels in the same color range

## Slide 8: Color-Based Object Extraction in Simulink
Image Blurring
Color Extraction
Result Blurring
Region Segmentation

## Slide 9: Simulink Model Demonstration

## Slide 10: Machine Vision
Convolution is one of the most common filtering and feature detection methods
  Cross-correlation computes the “similarity” between a local image region and a template
  Convolution computes cross-correlation (the sum of the product of the corresponding template and image pixels) for each template location
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 255 | 255 | 255 | 255 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 255 | 255 | 255 | 255 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
85
112
85
112
85
112
112
85 112 112
85 0 85 85
112 85 112 112
85 112 85 112 85

## Slide 11: Machine Vision
Edge Detectors:
  Roberts Templates:
  Sobel Templates:
0 | 1
-1 | 0
1 | 0
0 | -1
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
0 | 1 | 2
-1 | 0 | 1
-2 | -1 | 0
2 | 1 | 0
1 | 0 | -1
0 | -1 | -2

## Slide 12: Machine Vision
To extend the capabilities of vision, multiple special purpose types of cameras exist:
  Visual light cameras
  Near infrared cameras
  Heat cameras

## Slide 13: Heat Camera Demonstration

## Slide 14: Machine Vision
Unusual optics to change field of view and perspective
  Super fisheye lenses for 185 degree field of view
  Panoramic lenses for view in all direction

## Slide 15: PAL Lens Demonstration

## Slide 16: Machine Vision
Machine vision with a single camera has a number of advantages over other sensors:
  Images contain large amounts of information
  Object identity and behavior can be extracted
But single camera vision has also significant problems:
  Extraction of objects is very difficult
  Determination of distance requires assumptions
    Size is known
    Terrain is known

## Slide 17: Stereo Vision
Stereo vision allows to determine distance to an object using triangulation
Need to solve the correspondence problem
  Identify the same feature in both images
  Compute angles from the cameras to the feature
  Triangulate location
  Compute distance

## Slide 18: Stereo Vision
The correspondence problem is in general not tractable (or even not solvable)
Need either better algorithms or other methods to apply this on UxVs
  Even humans fall prey to the correspondence problem:
    E.g. Stereograms
  Computers without additional information are prone to make many mistakes

## Slide 19: Structured Light Sensors
Structured light is one way to address the correspondence problem
  Replacing one camera with a pattern generator means:
    Pattern location in one camera is known
    Pattern is easier to find in the other camera
  Laser striping is the simples form of structured light sensors

## Slide 20: Structured Light Sensors
Laser striping is limited to a very small number of lines to avoid the re-occurrence of the correspondence problem
  More complex, non-repetitive patterns can address this: E.g.: Microsoft Kinect 360
    Project a known, non-repeating pattern
    Identify region patches in the image
    Determine distance

## Slide 21: ASTRA Demonstration

## Slide 22: Structured Light Sensors
Structured light sensors require reliable identification of the projected pattern
  Pattern is difficult to find in bright conditions
  Distance can only be determined at the pattern-level (not at the pixel-level)
Structured light is generally limited in resolution and in terms of the environments in which it can be used

## Slide 23: Time-Of-Flight Cameras
Time-of-flight cameras compute the distance of a part of the object by measuring the time it takes for light to travel from a light source to the individual pixel
  Emit modulated light near lens
    Modulation changes intensity at a rate of around 15-30 MHZ
  Compute time-of-flight based on phase shift in modulation
    Eliminates the need to measure at 1/100 nanoseconds resolution
Modulated
Illuminator
TOF
Camera
Objects
Phase Shift
Calculation

## Slide 24: Time-Of-Flight Cameras
Time-of-flight cameras have recently become available
  Swiss Ranger
  Kinect One

## Slide 25: Swiss Ranger Demonstration

## Slide 26: Machine Vision
Different vision sensors are best for different applications
  Choice of wavelength and lenses can be important parts when deciding what vision sensors to put on a UxV
  While structured light and TOF systems are no longer passive, they make computing distance significantly easier
    Have to decide the tradeoff in terms of visibility and sensitivity to change in lighting
Identification of the object is a very difficult problem and in general not tractable

## Slide 27: Machine Vision
While vision sensors are an important sensor modality that provides information that is not available from other sensors, it is not a replacement
  Proximity / range sensors like LADAR are usually faster to evaluate and sufficient for collision avoidance
  Vision can be fooled by transparent surfaces and ones without easily discernable features
  Inclusion of vision is a significant commitment in terms of image processing algorithm development