## Slide 1: Autonomous Guidance and Sensing
Manfred Huber
Spring 2020

## Slide 2: Guidance & Sensing
Previous classes and projects provided the robot with waypoint navigation and obstacle avoidance
  Way points provided a priori
  Reactive trajectory between the waypoints
  Reactive obstacle avoidance
We will now deal with making guidance more autonomous
  Path planning and trajectory tracking
  Sensing for goal detection and obstacle mapping

## Slide 3: Tentative Timeline
 | 4/13 | 4/20 | 4/27 | 5/04 | 5/11?
Integration of Vision System |  |  |  |  | 
Camera mount and vision presentation |  |  |  |  | 
Autonomous mapping |  |  |  |  | 
Path planning |  |  |  |  | 
Path planning demonstration |  |  |  |  | 
Path planning report |  |  |  |  | 
Autonomous goal search and navigation demonstration |  |  |  |  | 
Final Report |  |  |  |  | 

## Slide 4: “Hardware" Modifications
Guidance and Mapping will use both the sonar and a vision system
  Sonar provides reliable obstacle presence
    No good obstacle location information
  Camera provides object identity and pose information
    Goal identification and obstacle mapping
Mount details of camera are important
  Visual range
  Ambiguity

## Slide 5: Camera Mounting
Height and viewing angle change location ambiguity
  Distance largely influences size of objects
  Distance also influences location in the image

## Slide 6: Distance Estimation from Single Camera Vision
With an inclined mounting angle and flat terrain the location in the image of points touching the ground indicates distance
  Objects move up in the image with distance
  Need to determine calibration between image coordinates and locations in the world

## Slide 7: Location Estimation from Single Camera Vision
With an inclined mounting angle and flat terrain the location in the image of points touching the ground indicates a location
  Y- coordinate indicates a distance from the camera
  X-coordinate indicates an angle from the center line of the Camera

## Slide 8: Location Estimation from Single Camera Vision
In a pinhole camera model pixel locations represent a “beam” relative to the centerline of the camera
  X and Y dimension of the image can be decoupled for two separate angles
    Additional information (e.g. camera angle and flat floor) allows to compute a location along the “beam”
y
α
f

## Slide 9: Camera Mounting
On flat ground the height of the bottom of an object in the image indicates its distance
  Larger inclination results in larger effect
  Inclination influences camera range
    Stronger inclination reduces range
Precision of determination is effected by many factors
  Camera height
  Camera vibrations
  Platform pitch and roll

## Slide 10: Camera Mounting
Camera mount has to provide visual range
  Objects should be detectable right in front of the platform as well as at large distances
    Tradeoff between mount height, mount angle, and field of view of camera
Camera mount should be stable to not increase vibrations
  Height increases vibration
  Height reduces stability of the platform

## Slide 11: Machine Vision
To determine the location in the image we have to apply machine vision
  Parts that belong to an object have to be identified
  Parts of the same object have to be combined
  Objects have to be separated from the background

## Slide 12: Machine Vision
By identifying and classifying groups of pixels as an obstacle, machine vision can be used to generate information that supports path planning, obstacle avoidance, goal finding, or opportunistic motion behaviors.

## Slide 13: Machine Vision
Many ways to process images or video have been developed
A common processing sequence to identify an object (object recognition) involves
Filtering
Feature
Detection
Segmentation
“Box”
Recognition
Early Vision

## Slide 14: Machine Vision
Filtering:
  Remove noise, normalize, and emphasize the image
Feature Detection:
  Extract significant local structures
    Edges, Color, Texture, Motion, …
Segmentation:
  Group features into regions belonging to a common object
Recognition:
  Determine identity of the object

## Slide 15: Machine Vision
Convolution is one of the most common filtering and feature detection methods
  Cross-correlation computes the “similarity” between a local image region and a template
  Convolution computes cross-correlation for each pixel
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 255 | 255 | 255 | 255 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 0 | 0 | 0 | 255 | 0
0 | 255 | 255 | 255 | 255 | 255 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
85
112
85
112
85
112
112
85 112 112
85 0 85 85
112 85 112 112
85 112 85 112 85

## Slide 16: Machine Vision
Edge Detectors:
  Roberts Templates:
  Sobel Templates:
0 | 1
-1 | 0
1 | 0
0 | -1
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
0 | 1 | 2
-1 | 0 | 1
-2 | -1 | 0
2 | 1 | 0
1 | 0 | -1
0 | -1 | -2

## Slide 17: Machine Vision
Common example for simple color-based object extraction:
  Filtering:
    Blur image to reduce noise in individual pixels
  Feature Detection:
    Identify pixels that are within a given color range
      Results in a black and white feature map
  Segmentation:
    Blob coloring to link neighboring pixels in the same color range

## Slide 18: Machine Vision and Obstacle Avoidance
Once objects are extracted as color blobs, their distance and location can be computed:
  Find parts that are in contact with the ground
    Lowes pixels of an object are potentially on the ground
      Represent the front of the object
  Translate pixel location to location in space
    Using the calibration of the camera pixel locations can be translated into floor locations
Starting from the bottom (closest objects) can help try to eliminate occluded obstacles
  For avoidance, only obstacles with particular distances are of interest

## Slide 19: Machine Vision Example
Image Blurring
Color Extraction
Result Blurring
Region Segmentation

## Slide 20: Next Tasks
Mount your camera
  Determine height and camera inclination
    A height around 10cm – 20cm off the chassis might be sufficient for a good distance range and still stable
    Inclination has to be adjusted according to the camera field of view
Acquire camera images in simulink
Establish image to world mappings with the camera
  We will provide a “horizon” during demonstrations

## Slide 21: Autonomous Waypoint Generation
In autonomous applications waypoints are often not easily available
  Vehicle should generate its own waypoints
Waypoints should be such that the generated trajectory through them does not collide with obstacles
  Waypoints have to be dense enough
  Waypoints need to be planned to consider obstacles in the environment
Path Planning provides a means for this

## Slide 22: Recap - Path Planning
How to move from a configuration A to a configuration B without hitting arbitrarily shaped obstacles
  Shape of robot makes this more complicated
    Thumper is largely a rectangle
  Movement constraints for robots lead to complications
    Thumper is unicycle type

## Slide 23: Recap – Configuration Space
The shape of the robot makes it more difficult to plan a path since no part of the robot can hit an obstacle
  Robot takes up a volume in Cartesian space
Configuration space is the space spanned by the degrees of freedom of the robot
  A point in configuration space describes the complete geometry of the robot
  In Configuration space the robot can be reduced to a single point

## Slide 24: Recap – Configuration Space
In Configuration space the robot can be reduced to a point by extending the obstacles appropriately
  A round, holonomic mobile robot can be represented in a 2D configuration space
  Other robot geometries can only be addressed accurately in a 3D (or higher dimensional)

## Slide 25: Thumper Configuration Space
The Thumper is a unicycle-type robot
  Can move forward and turn in place
  Treating it as holonomic does not lead to non-executable trajectories
    Only efficiency of execution can be influenced since it might have to stop and turn in place
The Thumper is largely rectangular
  Treating it as cylindrical influences completeness by increasing the minimum clearance required
Treating Thumper as holonomic and cylindrical allows for path planning in 2D

## Slide 26: Recap - Mapping
Multiple representations for map information have been used
  Occupancy grid maps:
    Map as array of obstacle/free cells
  Landmark-based maps:
    Map as a set of landmarks with poses
  Topological maps:
    Map encodes connectivity
Occupancy grids are often the simplest representation if the area to be mapped and the required precision are limited

## Slide 27: Recap – Basic Motion Planning Problem
Basic Motion Planning Problem in Configuration Space is a simplified path planning problem
  Solid robot reduced to a single point (by extending obstacles appropriately)
  Only static obstacles
  Holonomic robot
  Only collision free paths are allowed

## Slide 28: Recap - Path Planning Approaches
Roadmap approaches
  Construct a set of “roads” that the robot can move on
  Find a sequence of roads that lead from start to goal
Cell Decomposition approaches
  Decompose the space into obstacle cells and free space cells
  Find a sequence of connected free space cells such that the start is in the first and the goal in the last
Potential Field approaches
  Design a numeric function over the configuration space with the goal at a minimum and obstacles at a maximum
  Perform gradient descent to reach the goal

## Slide 29: Roadmap Approaches
Voronoi Diagram
  Road construction
    Construct road segments that are equidistant to the two nearest obstacle features (including the workspace boundaries)
    Connect start and goal to the nearest road
  Path search
    Find a sequence of road segments that leads from start to goal

## Slide 30: Approximate Voronoi Diagrams
Approximate Voronoi diagram can be generated easier using distance propagation methods
  Simultaneously starting wave fronts from all obstacles, record the points at which two wave fronts meet for the first time
    In practice this requires a discretization of the configuration space.

## Slide 31: Cell Decomposition Approaches
Approximate Regular Grid Cell Decomposition
  Divide space into a regular grid and mark cells that contain any piece of an obstacle

## Slide 32: Navigation Functions
Manhattan Distance
  Discretize space into a regular grid
  Label goal cells with a potential of 0
0
  Propagate increasing distances to neighboring cells
1
1
1
1
2
2
2
2
2
2
3
3
3
3
3
4
4
4
4
5
5
5
6
6
6
6
7
7
7
7
8
8
8
8
9
9
9
9
9
10
10
10
10
10
11
11
11
11
11
11
11
12
12
12
12
12
12
12
12
13
13
13
13
13
13
13
13
14
14
14
14
14
15
15
15
15
15
16
16
16
16
16
17
17
17
17
17
18
18
18
18
19
19
19
19
20
20
20
20
20
21
21
21
21
21
22
22
22
22
23

## Slide 33: Path Planning Approaches
Choice of path planning method changes the type of trajectories that are generated
  Optimal distance methods like Visibility Graphs or Manhattan Distance generate shorter paths but move very close to obstacles and generate paths with corners
  Distance/risk methods like Voronoi Diagrams of Harmonic Functions prefer paths with more clearance and generate smoother paths but result in longer overall paths
Path execution / trajectory tracking should take properties of paths into account

## Slide 34: Trajectory Tracking
To track the path generated by the path planner the guidance system has to generate waypoints for the robot to move towards
  A priori waypoint list generation
    A complete list of waypoints along the trajectory can be generated form the path
      Fixed path will be used, independent of errors in execution
      Transition between waypoints can result in control discontinuities
  Dynamic / “on the fly” waypoint generation
    Waypoints can be generated using the path planner results and the current location of the robot at every point in time
      Waypoints generated to have specific properties or distances
      Can be used to influence trajectory tracking dynamics

## Slide 35: Simulink Path Planning Example

## Slide 36: Next Tasks
Start building your path planner
  Determine what path planner you want to use
  Familiarize yourself with the provided Simulink model
  Build initial Matlab function for the path planner in the provided Simulink simulation model
Move your path planner to the robot