## Slide 1: Communications
Manfred Huber
Fall 2019

## Slide 2: UxV Communications
UxVs usually require reliable communications for operation
  Transmission of data from the UxV
  Transmission of commands to the UxV
Communications are important both inside and outside the UxV
  Between components on the platform
    Will deal with this later
  Between multiple UxVs
  Between UxVs and ground stations/terminals

## Slide 3: UxV Communications
UxVs communications started at the end of the 19th century
  First systems initially used wired communications
  Moved to wireless communications early on
    First wireless remote control UxV was a boat by Nikola Tesla in 1898
  Increasingly more complex use over time

## Slide 4: Communication in UxVs
Different forms of UxV systems utilize different communication architectures
  One-way remote control platforms
    Simple to implement
    Very low cost communications
    Significant need for human operators
    Requires strict line of sight to the platform

## Slide 5: Communication in UxVs
Sensor
Information
Control
Commands
  Two-way remote control platforms
    Allows operation without line of sight
    Higher power requirements on the platform
    High bandwidth requirements for return signals
    Need for real-time communications
    Significant need for human operators

## Slide 6: Communication in UxVs
  Partially autonomous platforms
    Reduced real-time requirements
    Reduced operator load
    Transmission of selective information
    Need for significant processing power and sensor suites on the platform
Status
Information
Control Modes

## Slide 7: Communication in UxVs
  Besides communication to the ground, UxVs also need means of intra-platform communication
    Allows to coordinate multiple platforms
    Need for significant processing power and sensors on the platform

## Slide 8: Communication Modalities
Wired communications
  Very simple and high throughput
  Relatively unaffected by environmental effects
  Relatively secure
  Severely limits the mobility of the platform

## Slide 9: Communication Modalities
Optical Communications
  Well focusable to limit interceptability
  Works under water for reasonable distances and speeds
    Up to 100 Mbps and more than 100m
  Requires line of sight

## Slide 10: Communication Modalities
Acoustic Communications
  Sound can transmit information without need for direct line of sight
  Works under water and in air
    Sound can travel very large distances in water
  Relatively low throughput communications
  Easy to intercept and interfere with

## Slide 11: Communication Modalities
Radio Frequency (RF) Communications
  Relatively high throughput
  Can potentially work without line of sight
    Depends on frequency used
  Can be focused to reduce interception and to optimize signal loss
  Signal quality depends on weather and environment conditions
  Does not work under water

## Slide 12: RF Communications
RF is the most common communication modality in all UxVs except for submarines
  Provides a good balance between cost, range, and data throughput
  Can be used omni-directional or in a directed line of sight fashion
    Different antenna designs can regulate signal characteristics
  Can have different characteristics in terms of signal penetration and range
    Choice of RF frequency influences characteristics

## Slide 13: RF Communications
As radio frequencies are shared, they are generally regulated and divided in bands
Civil Radio band designation
1-10 kHz VLF (very low frequency)
10-100 kHz LF (low frequency)
100-1000 kHz MF (medium frequency)
1-10 MHz HF (high frequency)
10-100 MHz VHF (very high frequency)
100-1000 MHz UHF (ultra high frequency)
1-10 GHz SHF (super high frequency)
10-100 GHz EHF(extremely high frequency)
US Military, Satellite, and Radar bands
1-2 GHz L Band
2-4 GHz S Band
4-8 GHz C Band
8-12 GHz X Band
12-18 GHz Ku Band
18-27 GHz K Band
27-40 GHz Ka Band
40-75 GHz V Band
75-110 GHz W Band
110-300 GHz mm Band
300-3000 GHz mm Band

## Slide 14: RF Communications
As a general rule of thumb, increasing the RF carrier frequency leads to
  Increased throughput
  Better ability to focus the signal
  Reduced object penetration capabilities
  Increased straight line transmission behavior
    Reduced atmospheric reflection
  Increased sensitivity to weather
There are exceptions based on the specific conditions and properties of the frequencies

## Slide 15: RF Communications
In RF communications a signal is modulated onto a carrier frequency
  Signal can be analog or digital
Throughput (or achievable data rate) can be influenced through multiple factors
  Carrier frequency
  Modulation scheme used
  Bandwidth (range of frequencies used)
  Multiple transmitters

## Slide 16: RF Communications
Range can be influenced by a number of measures
  Directional transmission
    Focuses energy in one direction
  High gain antenna design
  High sensitivity amplifiers
    But: can not overcome real signal interference/noise

## Slide 17: RF Communications
Range limitations are driven by signal dissipation and losses
  Free space signal loss due to signal dissipation
  Atmospheric absorption
    Ions in the atmosphere absorb RF energy
  Precipitation absorption
    Rain and snow absorb RF energy
  Signal interference
    Natural and artificial phenomena (lightning, solar flares, etc) can produce interference

## Slide 18: RF Communications
Choice of the appropriate RF communication scheme for a UxV should consider multiple factors
  Available frequency bands and allowed signal strengths
  Data rate requirements
  Real time requirements
  Environmental conditions
    Line of sight availability
    Interference or jamming risks
  Energy availability

## Slide 19: RF Communications
Modern UxVs often use multiple RF communication modes
Military Satellite
Commercial Satellite
Global Hawk example

## Slide 20: RF Communication Modes
Omni-directional for station and/or platform
  No need for antenna guidance
  Potential for signal broadcast
  Very fast decrease in signal strength
Directional point to point (line of sight) using parabolic/directional antennas
  Relatively large range with limited energy
  Reduced risk of interference, interception, and jamming
  Need for active antenna tracking

## Slide 21: RF Communication Modes
Mixed modes with directional transmit, omni-directional receive or vice versa
  Intermediate range
  Only partial antenna tracking problem
Relayed communication
  Satellite communication
    Wider coverage – potentially world-wide
  Relay UAV / UGV
    Dynamically establishable relays
    Smaller overall transmit distance

## Slide 22: RF Communication and Mission Requirements
Choice of transmission mode regulates a number of factors
  Throughput
  Range
  Coverage area
  Sensitivity to interference, noise, and jamming
  Time delay in communications

## Slide 23: RF Communication and Mission Requirements
Communication delays impact ability to remotely control UxVs
  Line of sight 2ms
  Low earth orbit 10ms
  Medium earth orbit 100ms
  Geostationary 200-300ms
With transmission relays above low earth orbit, direct remote operation of fast vehicles becomes risky
  GEA more than triples human reaction time

## Slide 24: RF Communication and Mission Requirements
Military Satellite
Commercial Satellite
UAVs and UxVs usually have multiple, potentially redundant communication links
  E.g. Glowal Hawk:
    - UHF (LOS command and control)
    - UHF (SatCom command and control)
    - CDL (J-band LOS down link)
    - SHF (SatCom Ku band down link)

## Slide 25: Wireless Communications
For low-end applications, satellite links and dedicated line of sight communications are often impractical and expensive
  Common technologies exist if infrastructure is available or only limited range is required
    Cell phone network / WiMax
      Limits altitude and excludes certain areas
    WLAN
      Can be self-deployed
      Limits range
    Mesh networking
      Allows dynamic formation of network
      Requires the deployment of relay points

## Slide 26: Wireless Networks
Affordable, self-deployable (open) wireless networks and frequencies are available with power limitations
  Analog remote control in the 40MHz or 900MHz range
  Digital wireless in the 900MHz, 2.4GHz, and 5.2GHz range
Additional services provide infrastructure on leased data channels
  Cell phone and WiMax services
    Operate at higher power and higher throughput

## Slide 27: Wireless Networks
Using wireless media, different types of networks can be established
  Point to point networks
    Direct communication between two transmitters
  Infrastructure-based networks
    Communication through an infrastructure access point
  Ad-hoc/mesh networks
    Communication through other nodes with automatic re-configuration

## Slide 28: Wireless Networks
Common standards for wireless systems
  802.11 a/b/g/n - WiFi
    WiFi provides infrastructure-based communciation (with the possibility for point to point communication)
      Relatively high bandwidth and range (<54Mbps , <2km)
      High computational and power overhead
      Requires consistent communication routes
      Easy configuration and use
    Most commonly operates on 2.4GHz or 5.2GHz

## Slide 29: Wireless Networks
  802.15.1 – Bluetooth
    Point to point communication
      Reasonable data rate (<24Mbps)
      Shorter range (<150m)
      Very low power requirements
      Generally no relay capabilities
      Easy configuration and use
    Most commonly operates on 2.4GHz

## Slide 30: Wireless Networks
  802.15.4 – Mesh Networking (e.g. ZigBee)
    Mesh Networking
      Lower data rate (<250Kbps)
      Longer range: high power (<8km); low power (<100m)
      Very low power requirements
      Dynamic network formation and package re-routing
      Built-in relaying
      Easy configuration and use
    Most commonly operates on 2.4GHz or 900MHz

## Slide 31: Wireless Networks
  802.16 – WiMax
    Long range infrastructure based networking
      High data rate (<70Mbps)
      Large range (<50km)
      Higher power requirements
      Requires established infrastructure
    Operates in a wide range of spectrums from 500MHz over 2.5GHz to 3.3GHz and 3.5GHz. Most commonly operates on 2.4GHz

## Slide 32: Wireless Networks
Point to point vs. Network
  Point to point communications usually take the form of wireless serial lines
    Single stream of data in each direction
    Usually lower overhead and delay times
    Higher data rates
  Networks allow more than two entities (processes or platforms) to communicate
    Arbitrary data streams can be initiated
    Multiple data streams can overlap

## Slide 33: Wireless Networks
Infrastructure vs. Mesh Networks
  Mesh networks provide extra flexibility by allowing to establish the network infrastructure dynamically
    Usable in disaster scenarios
    Usable in areas without established infrastructure
  Mesh networks have a higher overhead for transmitting packets due to route establishment
    Lower throughput
    Longer packet delay and round trip times
    More complex to initially configure
  The scenario and environment usually determines what is better

## Slide 34: Wireless Networks
Networks and network protocols are structured in multiple layers

## Slide 35: Protocols
Protocols manage data transfer standards
  Ensure that transmitter and receiver understand each other
  Protocols are layered according to the network layers

## Slide 36: Protocols
Link layer protocols handle hardware addresses
  Mostly using Media Access Control (MAC) addresses
Network layer protocols handle addressing
  Most commonly using Internet Protocol (IP) addressing
Transport layer protocols handle data transfer
  Transmission Control Protocol (TCP) for reliable, ordered, error-checked data transfer
  User Datagram Protocol (UDP) for transfer without handshakes

## Slide 37: Transport Layer Protocols
TCP and UDP are the most common internet transport protocols
  TCP provides reliable connections
    Handshaking, Collision checking, Error detection, Packet ordering
    Requires to re-transmit packets if transfer medium is unreliable (e.g. wireless signals)
  UDP operates on best effort basis
    Data is transmitted but transmission is not verified
    Packets are not ordered or error checked
      Provides mechanisms for checksums

## Slide 38: Transport Layer Protocols
In an unreliable medium such as wireless, the choice of protocol is important
  TCP provides guarantees but has pretty significant overhead
    Bandwidth use can be significantly higher than actual data transfer
      Re-transmissions of very large packages can bog down network due to significant chance of errors
    Back-off from collisions delays data transmission
  UDP is useful if some data loss is acceptable or if data has to be real-time
    Data is transmitted at a given rate

## Slide 39: Internet Protocols
The most common suite of protocols is the Internet Protocol suite
  IP protocols treat all traffic the same
    Traditionally no priorities
    No timing or ordering guarantees at the link layer
  Real time protocols are implemented in top of UDP
    No true real time guarantees
Priorities have been added to the network protocols but are not commonly used
  Priorities can be useful for UxV communication

## Slide 40: Application Protocols
Users interact with application layer protocols
  Application layer protocols define specific application components
    File transfer protocols (e.g. ftp, sftp, ftps)
    Remote session protocols (e.g. telnet, ssh, rfb)
    Data streaming protocols (e.g. rtsp)
    Hypertext protocols (e.g. http)
  Application layer protocols are selected according to the needs of the application
    Timing requirements
    Reliability requirements
    Data transfer requirements

## Slide 41: Wireless Security
Wireless transmission are usually prone to noise, interference, and jamming
  Wired and optical communications are usually harder to jam than acoustic and RF
  Directional line of sight transmissions are harder to jam than omni-directional transmissions
Wireless transmissions are generally interceptable
  Others can listen in
  Transmission content can be altered
  Transmissions can be spoofed

## Slide 42: Wireless Security
Multiple means can be taken to make communications more secure
  Physical means:
    Directional communications
    Use of difficult to operate in medium
  Error correction
    Error checking and error correcting codes can be used to identify transmission errors
  Encryption and authentication
    Encryption of the link and of the data protects against falsification of content
    Authentication protects against spoofing

## Slide 43: Wireless Security
Wireless networks use different types of encryption
  Network level authentication and encryption
    Authenticates clients and encrypts all network traffic
      Only authenticating clients can transmit and read/write packets
    E.g. Wired Equivalent Privacy (WEP) or WiFi Protected Access (WPA)
  Connection level authentication and encryption
    Authenticates/encrypts when establishing a particular connection
    E.g. Secure Sockets Layer (SSL)

## Slide 44: Wireless Security
Encrypted connections protect against interception as well as the willful injection of data
  No protection from jamming
  No protection against data loss
Encryption introduces computational overhead
  Encryption and decryption require additional computation
  Encryption and decryption slightly increase communication delays

## Slide 45: UxV Networking
A wide range of networking mechanisms exist for use in UxVs
  Network structure based on task needs
    Range requirements
    Number of UxVs
    Type of data to be exchanged
    Data loss implications
  Infrastructure or mesh networks can support mixed protocol types
    Use of overlapping protocol types influence each others performance
      E.g. UDP traffic delays TCP traffic

## Slide 46: UxV Communications
UxVs can use a wide range of communication mechanisms
  Different communication media
  Various network structures
  Different communication protocols
Platform and task characteristics should inform choice of communication setup
  Environment influences best communication medium and mechanism
  Task requirements determine network and protocol choices