## Slide 1: Obstacle Mapping & Vision
Manfred Huber
Spring 2020

## Slide 2: Guidance & Sensing
Previous classes and projects provided the robot with waypoint navigation, obstacle avoidance, and sensor fusion
  Way points provided a priori
  Reactive trajectory between the waypoints
  Reactive obstacle avoidance
  Path planning and trajectory tracking
We will now deal with making guidance more autonomous
  Sensing for goal detection and obstacle mapping

## Slide 3: Hardware Modifications
Guidance and Mapping will use both the sonar and a vision system
  Sonar provides reliable obstacle presence
    No good obstacle location information
  Camera provides object identity and pose information
    Goal identification and obstacle mapping
Mount details of camera are important
  Visual range
  Ambiguity

## Slide 4: Obstacle Sensors
We have already used sonar sensors for obstacle avoidance
  Sonars are good at
    Determining the presence of an obstacle / object
    Measuring the distance to this obstacle
  They have problems with:
    Identifying the object
    Differentiating multiple objects
Sonars can be used for mapping
  Limited by the size of the senor cone

## Slide 5: Sonar-Based Mapping
We have to assume that everything visible by the sonar is an obstacle
  Determining distance and shape of sonar cone potential obstacle bins can be identified

## Slide 6: Sonar-Based Mapping
Sonars have disadvantages for mapping
  Spatial resolution is limited by the width of the sonar cone
  Sonar can be noisy due to environmental effects
    Reflected signals are not received
    Signals are only received after multiple reflections
    We have to assume that everything visible by the sonar is an obstacle
Sonars are better for obstacle avoidance than for mapping
  Vision or Laser rangers are preferred for mapping

## Slide 7: Vision-Based Mapping
Single camera vision systems have different properties from sonar sensors
  Vision sensors are good at
    Identifying the identity of objects
    Determining the shape, color, and other features of objects
    Determining location in image coordinates
  Single camera vision has in general problems with
    Determining distance to objects
For mapping the mapping from image to space has to be addressed

## Slide 8: Obstacle Location
To determine the location in the image we have to apply machine vision
  Parts that belong to an object have to be identified
  Parts of the same object have to be combined
  Objects have to be separated from the background
  Parts in contact with ground give location

## Slide 9: Machine Vision and Obstacle Mapping
Once objects are extracted as color blobs, they can be mapped to obstacle locations:
  Find parts that are in contact with the ground
    Lowes pixels of an object are potentially on the ground
      Represent the front of the object
      For objects that are flat on ground, all of the blob gives size
  Translate pixel location to location in space
    Using the calibration of the camera pixel locations can be translated into floor locations
  Map locations to obstacle cells
Starting from the bottom (closest objects) can help try to eliminate occluded obstacles

## Slide 10: Single Camera Obstacle Mapping
Find obstacles locations in the image
  Find obstacles
    We are using color-based identification
  Identify size and location of obstacle in image
    Blob-coloring identifies bounding box an center
Translate image location to vehicle location
  Camera calibration provides translation
    Translation table is simples solution
    Since all objects are on the ground, full size can be used
Translate vehicle location to obstacle grid location
  Odometry is transform (rotation and translation)

## Slide 11: Mission Setup (Gazebo View)
xo, yo,
odometry
*
X
Y
Start
known obstacles
Unknown (“dynamic”) obstacles
*
xi, yi
Image
xv, yv
Vehicle
xv, yv
Vehicle
x, y
Obstacle
Obstacle:

## Slide 12: Next Tasks
Integrate Vision Component into Mapping
  Use your vision system to determine locations of unknown obstacles
    Add unknown obstacles to the map
    Trigger recalculation of the path if needed
  Use vision system to get you closer to the goal
    Can improve path by localizing goals and obstacles
Known obstacles (blue), unknown obstacles (green), goal (yellow) have different color
Bonus: Include obstacle avoidance for cones
  Use sonar but consider how to avoid without hitting other obstacles

## Slide 13: Tentative Timeline
 | 4/13 | 4/20 | 4/27 | 5/04 | 5/15
Integration of Vision System |  |  |  |  | 
Camera mount and vision presentation |  |  |  |  | 
Autonomous mapping |  |  |  |  | 
Path planning |  |  |  |  | 
Path planning demonstration |  |  |  |  | 
Autonomous goal search and navigation demonstration |  |  |  |  | 
Final Report |  |  |  |  |