## Slide 1: Obstacle Detection and Avoidance with Simulink using Sonar and LIDAR Sensor
Adapted from Atilla Dogan
XX {4,5}379 – Unmanned Vehicle System Development
Spring 2020

## Slide 2: Sonar Range Sensor
Range
detection
varies with
factors
such as
size,
shape,
etc of
the obstacle

## Slide 3: Sonar Sensor Model in Simulink
The first step for developing obstacle avoidance algorithm is to have a sensor model in simulation
A simple sonar sensor model is developed for Simulink
  Sensor coverage is assumed to be rectangular and parameterized
  Obstacles are assumed circular (or square)
  Sensor model gives a range data when the obstacle is within sensor coverage

## Slide 4: Sensing Model
hs
as
bs
rs
rs is the range
measurement
received from
the sensor
model

## Slide 5: Simulink Block
A simulink block is developed representing sonar sensor
position in xy-frame
& radius of multiple
obstacles
UGV position
in xy-frame & angle
Range to
the nearest
obstacle

## Slide 6: Sonar Block Implementation
Sonar Sensor in UGV (tank) model
Encoders in UGV

## Slide 7: New Tank (Thumper) Model
Outputs:
Before:
Right & Left Encoder Counts
Now:
One more output =
range to closest obstacle
if within range

## Slide 8: GNC takes SonarRange Measurement
Additional
input to
GNC:
to be used
for obstacle
avoidance

## Slide 9: Parameter File for Obstacles & Sonar Sensor
1st obstacle
2nd obstacle
3rd obstacle
You can add more
x-coordinate
y-coordinate
radius
Sonar sensor parameters

## Slide 10
Three obstacles

## Slide 11: Example: Output of Sensor Model
767: no detection
Distance to
obstacle in cm

## Slide 12: MATLAB/Simulink Files Provided
You will be given a folder
Main Simulink Model
Tank subsystem w/ sonar model
GNC subsystem for
wayPoint navigation
(no obstacle avoidance capability)
GNC parameter file
Obstacle/SonarSensor parameter file
Vehicle parameter file
Animation runs after sim
plotting after sim

## Slide 13: Run Simulation
Download “pp11_simModelObst2students.zip” zip-file from blackboard
Run simulation in folder
  To demonstrate the details of the simulink model, sonar sensor output and the animation

## Slide 14: Your Assignment - Simulation
Add additional logic to GNC to avoid obstacles and still go through wayPoints
based on obstacle range measurements from sonar model

## Slide 15: Modified GNC - Example
I have modified the current Guidance Subsystem to add obstacle avoidance capability
Commanded Angle is computed
based on SonarRange as well as
heading towards the wayPoint

## Slide 16: Modified GNC - Example
Three obstacles
are avoided nicely

## Slide 17: Steps for Assignment
Develop Simulink Block to read sonar range measurement into your Simulink model.
Connect GNC subsystem with teensy sensor and motor blocks