## Slide 1: GNC Implementation in NUC for wayPoint Navigation
Adapted fromAtilla Dogan
XX {4,5}379 – Unmanned Vehicle System Development
Spring 2020

## Slide 2: Simulation Model
Download “simModelUGV_ClosedLoop.zip” from blackboard
Simulink Model: trackVehicleNewVer6b_Encoders_DR_GNC.slx

## Slide 3: Simulation Model
For controlling the actual UGV,
we only need GNC
We will have the actual vehicle
instead of this block

## Slide 4: Simulink Model for NUC
Need to build a new simulink model
  “GNC” block
    for Guidance, navigation, and Control
  “Set Pace” block
    to ensure simulink model runs at the speed of real time
  ROS Encoder position Subscriber block
    to read in encoder counts coming from the Teensyboard
  ROS Motor Velocity Publisher block
    to send out %duty cycle commands to the electric motors through the Teensyboard

## Slide 5: Simulink Model for NUC
When this simulink model is run in NUC,
which is connected to the teensy on the UGV,
UGV should be steered through the waypoints specified